Elite Playground Inspections

| Customer Name: Frampton PC | Site Name: The Loving Memorial Field | Site No: 1 | Inspected By: | Date: 12/03/2019 |
| --- | --- | --- | --- | --- |

| Main play area surface: Grass | Type of Fencing: Various Chain-link | No of Gates: 2 | Self Closing: 2 | Non Self Closing: 0 |
| --- | --- | --- | --- | --- |

| Manufacturer | Year | Description | OK | WP | Surfacing | OK | WP | Comments |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Europlay | 2008 | 2 Cradle Seat Swing |  |  | Grass Mat |  |  |  |  |
| Europlay | 2008 | 4 Seat Horse See Saw Springer |  | 3 | Grass Mat |  |  | Ply seats are worn at the edges, showing signs of rot in the beam, handle is loose & 4 have been broken off – sand down & paint edges. Tighten handle if possible & replace others, monitor & replace rotting beam when necessary. |  |
| Europlay | 2008 | Horse Springer |  | 2 | Grass Mat |  |  | Ply seat & one side are worn at the edges - sand down & paint edges where necessary |  |
| Nijha | 2008 | Bicycle Carousel |  | 1 | Grass Mat |  |  | Paintwork worn on the seats - sand down & paint |  |
| Europlay | 2008 | Multi Play Unit |  | 3 1 1 | Grass Mat |  |  | Rot in some of the timber work has appeared, this includes the barriers, platforms, tunnel & ramp (including one post) – repair/replace & treat/paint timber to suit Paintwork has worn at the edge of the slide chute – sand & repaint timber where necessary Bolt cap missing – replace cap |  |
| Europlay | 2008 | Agility trail |  | 2 1 3 1 | Grass Mat |  |  | Rot in some of the timber work has appeared in the hanging steps – monitor condition Rope fixtures appear that they are loose but they are not Fixing missing to support beam to rope walkbridge & one post is loose or rotten in the ground – replace Bolt cap missing – replace cap |  |
| Europlay | 2008 | 2 Flat Seat Swing |  | 2 3 3 | Grass Mat |  | 3 | There is corrosion in the red support brackets – sand down & repaint. Seat not hanging correctly – adjust chain to suit. Surface needs repair Seats degrading – one at fixings underside, the other is cracking at the edges – replace seats. |  |
| Not Known | N/K | Backless bench |  |  |  |  |  |  |  |
| N/K | N/K | Picnic Table |  |  |  |  |  |  |  |
| N/K | N/K | Litter Bins |  | 2 |  |  |  | Green bin lid damaged & not locked – repair lid & keep locked |  |
| MGC | N/K | Pedestrian Gates |  | 2 2 |  |  |  | Fixings missing to both gates – replace fixings Potential trip hazard at gate to path nearest houses – reinstate ground/fit grass mat. Both shut too fast – adjust gate speeds to be between 4 - 8 seconds |  |
| N/K | N/K | Fencing |  | 2 2 4 |  |  |  | Iron work out of shape by road – monitor & replace if necessary Excessive bolt threads by gate near houses – remove & smooth ends of threads Area not dog proof due to large gaps in high fence leading up to goal posts – fill in missing fencing |  |
|  |  | Signs |  | 2 |  |  |  | Fixings missing to both, one is laying on the ground – refit sign and replace missing fixings |  |
|  |  | Outside Play Area |  |  |  |  |  |  |  |
| Not Known | N/K | Aerial Runway |  |  | Grass Mat |  |  |  |  |
| Lappset | 2006 | Basketball Goal |  |  | Grass Mat |  |  |  |  |
| N/K | N/K | Goal Posts |  | 1 | Grass |  | 1 | Goal post is corroded at the top beam one end – sand & paint The ground is slightly eroded – monitor & reinstate ground when necessary |  |
| N/K | N/K | Litter Bins |  |  |  |  |  |  |  |
| N/K | N/K | Fencing |  | 4 3 4 |  |  |  | Not dog proof. Chain-link is damaged, or missing, tension wires are broken around the perimeter, brambles are growing through or over the fence – repair/replace chain-link etc, remove brambles etc from fence near end of Aerial Runway Excessive bolt threads by gate near new gate – remove & smooth ends of threads Fence posts all rotten near houses – replace posts |  |
| N/K | N/K | Pedestrian Gate |  | 3 |  |  |  | This gate is locked. Fence post next to it is rotten – replace post |  |
| N/K | N/K | Vehicle access gate |  |  |  |  |  |  |  |
| FPC | 2018 | New Vehicle access Gate |  | 2 |  |  |  | Gap underneath at one end so not dog proof |  |

| Work Priority Guide |  |  |  |  |
| --- | --- | --- | --- | --- |
| 1 | Very Low | 3 | Medium |  |  |  |  |  |
| 2 | Low | 4 | High |  |  |  |  |  |

Maintenance Work Carried Out:

General Observations: